## Slide 1
REMAINING USEFUL LIFE
PREDICTION OF TURBOFAN ENGINES USING A HYBRID CNN-BILSTM-ATTENTION MODEL
A Research Project Based on the NASA CMAPSS Dataset
Khamalesh Ramesh
MSc in Data Analytics
x23325216
National College of Ireland

## Slide 2
Introduction to Predictive Maintenance in Aviation
Advanced ML methods revolutionize aircraft maintenance through predictive failure detection reducing AOG incidents and enhancing operational efficiency.
Aircraft Engine Maintenance Types:
1. Corrective: Fix after failure
2. Preventive: Scheduled
3. Predictive: Data-Driven
Why Predictive Maintenance?
Turbofan engines are complex and demand performance + reliability
FAA: 1 failure / 375,000 flight hours
MRO Market: $37.11B (2023) → $47.74B (2029)
RUL Prediction Types:
1. Model-based
2. Data-driven
3. Hybrid

## Slide 3
Research Question
How can a hybrid CNN–BiLSTM model, combined with adaptive noise filtering and
domain adaptation techniques, improve the accuracy and generalizability of
aircraft engine Remaining Useful Life (RUL) prediction using the NASA C-MAPSS dataset?
Research Objectives
1. Design a hybrid deep learning architecture using CNN, BiLSTM, and dual attention.
2. Preprocess sensor data with:
· Wavelet denoising
· Rolling statistics
· Delta features
· Normalization
3. Enhance robustness using composite loss (MSE + Huber) to balance outlier sensitivity.
4. Automate tuning using Optuna for hyperparameter optimization across datasets.
5. Evaluate model performance using:
· RMSE (Root Mean Square Error)
· MAE (Mean Absolute Error)
· R² (Coefficient of Determination)

## Slide 4
Previous Approaches in RUL Prediction
1. Physics-Based Models
· Use degradation laws, Kalman/particle filters for simulating engine wear
· Limitations: Require deep domain knowledge, poor adaptability to real-world noise
· Zheng et al. (2017): Extended Kalman Filter – RMSE: 192.7 vs. 255.8 (PF)
2. Shallow ML Models
· SVR, Random Forests, MLPs on handcrafted features
· Sherifi (2024): BiLSTM (RMSE: 23.18) outperformed RVR (RMSE: 31.30) on FD002
· Limitations: Fail to capture long-term temporal dependencies
3. Deep Learning Models
· LSTM, BiLSTM, CNN-BiLSTM architectures
· Abedin (2024): LSTM outperformed SVR/MLP on CMAPSS
· Wu et al. (2020): BiLSTM – strong on FD001 (RMSE: 13.65) but weak on FD004 (RMSE: 24.86)
· Limitations: Overfitting, weak generalization, no interpretability
4. Hybrid Architectures with Attention
· CNN–BiLSTM models enhanced with CBAM, dual attention, or EMD fusion
· Guo et al. (2023): Dual Attention – RMSE: 12.25 (FD001) to 19.86 (FD004)
· Zhang et al. (2024): CBAM attention boosted FD001 interpretability
· Limitations: Mostly tested on FD001; high computational cost
5. Signal Denoising & Optimization
· Few studies used adaptive noise filtering like wavelets
· Zhao et al. (2024): CSI-EMD + CNN–BiLSTM – promising but unstable at signal edges
· Yildirim & Rana (2024): Used Optuna for BiLSTM tuning (only on FD001)
· Limitations: No generalizable, tuned pipeline across FD001–FD004
Identified Research Gaps
· Weak generalization across CMAPSS subsets
· Lack of robust noise filtering
· Rare use of interpretable models or automated tuning methods

## Slide 5
NASA C-MAPSS Dataset
A realistic simulation dataset for aircraft engine degradation modeling.
Preprocessing Pipeline
1. Sensor Pruning: Remove low-variance or flatlined sensors to reduce noise
2. Wavelet Denoising (db4): Smooth high-frequency noise using Discrete Wavelet Transform
3. Normalization: MinMaxScaler + Yeo-Johnson PowerTransformer to reduce skew
4. Temporal Feature Engineering:
· Rolling mean & std (5-cycle window)
· Delta (first difference) features
5. Sequence Generation: Overlapping sequences of 20–35 cycles (subset-specific)
6. RUL Labeling: Piecewise-linear label strategy with cap at 125 for stability

## Slide 6
Hybrid CNN–BiLSTM–Attention Model for RUL Prediction
Core Components
1. Multi-Kernel 1D CNNs
· Three parallel Conv1D layers with kernel sizes 3, 5, and 7
· Capture local degradation patterns across different time scales
2. Bidirectional LSTM (BiLSTM)
· Learns temporal dependencies from both past and future cycles
· Outputs a rich, bidirectional representation of engine wear trends
3. Dual Attention Mechanisms
· Feature-wise Attention: Focus on informative sensors (e.g., S7, S13)
· Temporal Attention: Highlight critical time steps (e.g., onset of rapid degradation)
4. Regression Head
· Fully Connected Layers → Scalar RUL Prediction
· Output shape: [batch_size]
5. Composite Loss Function
· Combines MSE (sensitive to large errors) + Huber (robust to outliers)
· Enables noise-resilient learning on complex datasets (e.g. FD004)
Flow Diagram:

## Slide 7
Why Hyperparameter Tuning?
  Deep models are highly sensitive to parameters like:
  Sequence length
  Batch size
  Dropout
  Learning rate
  Manual tuning is inefficient and prone to overfitting
Optuna Optimization Setup
  Framework: Optuna (Bayesian optimization + pruning)
  Objective: Minimize RMSE on validation set
Optuna-Based Tuning Across CMAPSS Subsets
Search space:
Best Configs per Subset:

## Slide 8
Performance Across CMAPSS Subsets
Results Overview:
Key Observations
1. Consistently high performance across all datasets with R² > 0.99
2. Lowest errors in FD001 due to single fault and operating regime
3. Slightly higher errors in FD004 due to complex multi-regime + multi-fault nature
4. Dual attention + wavelet denoising provided strong generalization
5. Composite loss helped stabilize training under sensor noise and outliers
6. Results validate the pipeline’s ability to scale from simple to complex degradation patterns

## Slide 9
Modular, Interpretable, and Deployment-Ready Framework
Modular Architecture:
  Organized into clean functional layers:
  Promotes clarity, easy debugging, and rapid experimentation
End-to-End Reproducibility:
  Every step from raw data to prediction is logged and versioned
  CSV snapshots at each preprocessing stage
  Metrics and predictions stored in a structured format for analysis and review
  Ensures consistent results across different runs with fixed random seeds
Interpretability by Design:
  Feature-wise attention: Focuses on most informative sensors
  Temporal attention: Identifies critical time windows in engine life
  Transparent architecture: Each layer contributes interpretable insights
Real-World Integration Focus:
  Trained models are saved and reloadable for live inference
  Logs, plots, and checkpoints structured for audit and deployment
  Compatible with low-latency predictive maintenance systems

## Slide 10
Conclusion & Future Scope
Summary of Contributions:
1. Developed a hybrid CNN–BiLSTM–Attention model for accurate RUL prediction
2. Integrated wavelet-based denoising, temporal feature engineering, and composite loss to handle noisy, real-world data
3. Applied Optuna-based tuning across all CMAPSS subsets for maximum generalization
4. Achieved state-of-the-art results with R² > 0.99 on all subsets
5. Modular design ensures traceability, reproducibility, and interpretability
Future Enhancements
1. Explore Transformer-based architectures (e.g., TFT, Informer)
2. Add SHAP or LIME for improved explainability
3. Deploy to edge systems with model pruning and quantization
4. Combine with physics-informed modeling for hybrid learning
5. Expand application to other industrial sensor datasets

## Slide 11
Thank You !!